.he FidoNet Operating and Installation Manual        Page #
.mt 8
                      F I D O N E T 

   O P E R A T I O N    A N D    I N S T A L L A T I O N

                       M A N U A L 

                        Version 8
                       T. Jennings
                        1 June 84




     This manual explains (hopefully) what FidoNet does, how�
it does it, and how to install and run it. FidoNet is�
contructed as an add-on to Fido, and is not required, though�
it is recommended, as FidoNet  will be used to inform Fido�
BBS's of updates, bugs and other interesting things.

     It is required that you have a working Fido Bulletin�
Board system running before attempting to use FidoNet. There�
are plans to support non-Fido systems (MSDOS, PCDOS and CPM)�
in the near future, so that all can use FidoNet. For now,�
the packet format is described at the end of the FidoNet�
Operation chapter. Packets are transferred via XMODEM�
checksum or CRC, or TELINK checksum or CRC protocol.

     Please read the FidoNet Operation chapter for details�
on how Fidonet works; briefly, FidoNet is a method of�
connecting many BBS's in different locations for the purpose�
of transferring messages (and files) automatically. The net�
operates for a short period of time each day; for instance,�
Fido the Bulletin Board runs for 23 1/2 hours each day, and�
Fidonet for 1/2 hour. During this 1/2 hour, any messages�
marked as mail are combined into packets, and transferred to�
the each of the Fidonet programs. They are then unpacked,�
and normal BBS operation resumes.

     There are numerous things to control the setup, such as�
available systems, cost control (or prevention) and so on.�
Once setup, FidoNet is totally automatic, requiring no sysop�
or user intervention.
.pa
Before You Start 

     As of yet, there is no formal distribution method for�
FidoNet. Luckily, it consists of a single file, and shares�
the system files with Fido. You must have a Fido BBS system�
running first.

     To get FidoNet, download it from Fido #1, or any other�
system. Obviously you have this doc file; it contains all�
the information you need (I think ...) to setup FidoNet.

Important Note:

     Once you have a Fido BBS or FidoNet up and running,�
please, either call Fido #1 (415)-864-1418, 24 hrs, 1200/300�
and fill in the questionaire, or otherwise send me the�
following information:

     Sysops name,
     Systems name, if any,
     System phone number,
     Hours of operation,
     Hardware installed on,
     City and state,

     This is needed to control the assigning of node�
numbers. Without a valid node number, and without formally�
announcing your system, you will not receive any mail, no�
other system will have you in their node list.

     If you do this, you will receive mail from Fido #1,�
giving you your permanent node number, and a copy of the�
latest node list, which contains the other systems currently�
in the net. This list will be broadcast to all nodes for�
updates.
.pa
FidoNet Description

     Fidonet is a simple homogenous dialup network, to link�
Fido based Bulletin Board systems together for the purpose�
of automatic message transfers. Future enhancements are�
message forward and hold, file-attach, demand non-routed�
message transfers, and some form of true routing control.

     The current scheme supports only point to point�
messages. There is a BROADCAST message type, usable only by�
SYSOP level users, that are mailed to every node in the�
system.

     The original design was built around the current�
Bulletin Board architecture (if there is such a thing) which�
is basically: an unknown number of completely independent,�
standalone systems, with extremely low overhead in both�
maintenaince and cost. FidoNet was designed to be compatible�
with this, in that it should be:

     (1)  No extra work for the sysop,
     (2)  No effect on normal BBS operations,
     (3)  No unexpected extra costs,
     (4)  No effect upon system reliability.

     FidoNet is totally automatic, and requires no extra�
work, once set up. Other than the effect of allowing�
network-wide message traffic, the only other affect to the�
current BBS is that it is "down" to normal (human type)�
traffic during the mail period. This period is currently one�
half hour in the early morning.

     Costs, if any, are controlled by the sysop. Unless�
specifically enabled, mail will not be sent out from a node.�
(Sending mail costs; receiving mail is free) Fido version 8�
provides accounting and cost limitation functions (all�
automatic) to prevent unauthorized mail from being sent.�
There can also be "free" traffic to non-toll call nodes. The�
usual privelege levels can be applied to each of the Mail�
commands, to control their use.

     FidoNet message traffic success/failure does not in any�
way affect BBS operation. (Unless of course of hardware or�
other unavoidable failure.) Failure to make a connection and�
transmit a packet, or errors during incoming packets, affect�
only the mail sent or received. In the case of transmission,�
the messages will not be sent, nor will charges (if any) be�
applied to the senders credit account. 

     For a paying system, the sysop must occasionally set�
the users credit, using the SYSOP command. If reasonably�
large sums are used as a minimum ($20.00 or more) this will�
not need to be done more than once every few months.
.pa
Costs

     Each node maintains a node list, that contains the�
accessible remote systems. Systems not in the list cannot be�
mailed to. The sysop controls this file, updating or�
changing it with any text editor. It can only be read from�
within Fido.

     If the system is a public "free" one, then probably no�
toll call systems will be allowed for general use. All users�
credits default to zero, so that mail will not be allowed to�
non-free systems. Toll call systems can always be accessed�
by the sysop.

     There are also a number of ways to control access to�
the mail area; these are described in more detail in�
INSTALL.DOC and BBS.DOC.

     If a system in the node list is marked as free, then�
anyone may send messages to it.

     Fido controls all costs; Fidonet merely balances the�
accounts after messages are sent sucessfully.

     Each user record contains a credit and a debit.�
Messages entered are charged to debit, and cannot exceed the�
credit. Deleteing a message (that has not been sent yet)�
entered lowers the debit by the cost of the message; the�
actual cost of the message is stored within the message.
.pa
FidoNet Operation

     Fido and FidoNet are two complmentary programs, run one�
after the other on a daily basis. Currently, Fido runs 23�
hours a day, with FidoNet running for one hour. During the�
23 hours of Fido operation, messages may be entered as mail.�
The messages may be destined to any one or more of the�
available remote nodes in the nodelist.

     At the predetermined time, Fidonet takes control. It�
then (if enabled) creates mail packets, one per node,�
containing the messages for each node. If there is no mail�
to a node, no packet is created, and no call is made to that�
system.

     After the outgoing packets are made, FidoNet�
alternately waits for calls and attempts to place calls.�
Mail packet transfers are done on a simple collision�
detection basis. If there are a number of nodes to send mail�
to, each one is called in turn, until all are sent, or mail�
time is over. If it fails with one node, it goes to the�
next, and repeats the failed one only after trying all of�
the others first. The list of nodes to call is created in a�
semi-random order, depending on the order in which the�
messages we actually entered.

     In between outgoing calls (if any) FidoNet delays a�
random interval, during which it checks for incoming calls.�
This interval, along with the redial algorithm, synchronizes�
the net after the initial collisions.

     If an incoming call is detected, it attempts connection�
with it. The baud rate is determined (same as Fido) and a�
message to human callers is displayed (warning them that it�
is accepting only other FidoNodes) and a synchronization�
process is started. This process must complete within 60�
seconds, or the call is terminated. Once synchronized, the�
packet transfer is made. The receiver just stores that�
packet for later use, and then disconnects.

     To place an outgoing call, the sender dials the number,�
performs the sync process mentioned above, and transfers�
it's outgoing packet. (Messages to a given node are again�
checked against the node list at mail time; if they do not�
match, the packet is not sent, and an error is logged.) If�
the transfer was successful, the destination node number is�
deleted from the senders list of nodes to call. 

     The collision detect algorithm is optimized such that�
during the first few minutes of mail time, there are many�
collisions, after which the net synchronizes, and none or�
few collisions occur. Of course assumptions have been made�
on average traffic per node; for heavy (or low) traffic�
nodes, the collision algorithm can be modified by command�
line parameters.

     When mail time is over, FidoNet deletes all it's�
outgoing packets that were assembled, and for each one that�
was sent sucessfully, marks those messages (in the mail�
area) as SENT, so the originator can tell if they went out�
or not. Then, the incoming packets are unassembled, and the�
messages placed sequentially in the mail area. These packets�
are then deleted. If a packet was received that is not�
addressed to the node, it is deleted without unpacking and�
an error logged.

     If any mail at all was sent, the user file credits are�
balanced. This is somewhat unsatisfactory, as it balances�
the accounts even if the mail was not sent. This is to�
prevent extremely long processing time necessary to account�
for each message and user. (Users lists run upwards of 600�
entries typically; on a floppy based system this would�
become unworkable.)

     Fidonet then terminates, and if there were no fatal�
errors (disk full, etc) invokes Fido for another day.�
Messages received are then accessible like any other�
message.
.pa
Mail Packets

     Mail packets consist of a header (FidoNet overhead)�
followed by the message text in a compact form. (Text�
compression is not done in version 8 of FidoNet.)

     The header contains time, date, originating and�
destination node information, and so on. The exact contents�
of a packet follows. The header is never compressed.

     The message is broken into a number of variable length�
fields, and null terminated. Each message is preceeded with�
a message type; the only two defined today are Message,�
File, and EndOfPacket.

     Messages are reexpanded and assigned message numbers on�
the receiving end. Messages within a packet are independent;�
it is possible to receive part of a packet, and recover the�
messages that were sent sucessfully. The sender will�
consider the packet transfer a failure, though, and may�
later resend it.

     File type is not implemented yet.
.pa
Message and Packet Formats

/* Message packet header. */

struct _hdr {
     int orig;      /* originating Node # */
     int dest;      /* destination node */
     int year,month,day,hour,minute,second;
     int rate;      /* baud rate */
     int extra[20];
};
     The message, as contained in the packet, is not a fixed�
structure, but a continuous stream with markers. Each field�
is a minimum of one character, a null. Therefore, a totally�
blank message is 11 bytes; 3 integers, followed by one null�
for each text item. The fields are:

     int msgtype;   /* 1 == msg, 0 == EOF */
     int attr;      /* attribute */
     int cost;      /* in cents, */

     date;          /* null terminated date */
     to;            /* null terminated To: */
     from;
     subj;
     text;


This is the format of a message, as stored within Fido.

/* Message header structure. The message text is just a long�
string. */

struct _msg {
     char from[36]; /* who from, */
     char to[36];   /* who to, */
     char subj[72]; /* message subject, */
     char date[20]; /* creation date, */
     int times;     /* number of times read, */
     int dest;      /* destination node, */
     int orig;      /* originating node */
     int cost;      /* actual cost of msg */
     int caca[6];   /* extra space, */
     unsigned reply;/* previous (reply-to) */
     int attr;      /* message type, below */
     int up;        /* next (replied-to) */
};
.pa
Installation of FidoNet

     Assuming you already have Fido running, installing�
FidoNet is simple. (If you do not have Fido running yet,�
please refer to INSTALL.DOC)

     The basic steps to do are:

(1)  Set the basic mail parameters shared by Fido and 
     FidoNet.

(2)  Set up the MAIL message area.

(3)  Make up a working node list (list of other systems.)

(4)  Modify RUNBBS.BAT to automatically run Fido and 
     FidoNet.

(5)  Once running, get a permanent node number, and 
     inform Tom Jennings at Fido #1 of your system. (So 
     it can be distributed to others in FidoNet.)

     That is all there is to it. Each step is described�
below. Also, I can't emphasize how important it is to ...

     HAVE THE TIME AND DATE SET ACCURATELY!!!!!!!!

     Fidonet depends heavily on the correct time. Within 10�
minutes or so is fine, its not that critical, but since this�
is currently a time driven system, it is very important.

.pa
Setting the Basic FidoNet Parameters

     First, you must specify the basic net parameters, so�
that FidoNet (the program) can know where to find and put�
the mail. This is done with the 4 command. The parameters�
that need setting are:

     Node Number
     Mail Path
     Fudge Factor

     (Please see the Fido Manual Update for a description of�
the 4 command.) 

     Each Fido node in FidoNet has a unique number. To get a�
number, do the following:

(1)  Use 65535 as a temporary node number

(2)  Call Fido #1, and fill out the questionaire using the A�
command, or, send me, in a message or FidoNet Mail (node #1)�
the following information:

     Sysops Name
     Your Systems name (if any)
     Your systems phone number
     Hours of Operation
     Acceptable baud rates
     City and state
     Any other pertinent info

     And you will receive, via FidoNet mail, a copy of the�
latest node list and a permanent node number.

     If you do not set the node number (the default is zero)�
you will not be able to send or receive mail.

     The mail path is the full pathname of the message area�
you have assigned as a MAIL area. This is a bit redundant as�
far as Fido is concerned, but this is what is used to tell�
FidoNet what the mail area is. MAIL.SYS is shared between�
Fido and FidoNet.

     The Fudge Factor is a temporary measure used to�
compensate for cost estimate errors. It can be set anywhere�
from 0.5 to 2.0. All costs presented to the user are�
multiplied by this factor. Leave it at the default of 1.0�
until you figure out what the error (if any) is.
.pa
Setting Up a Mail Message Area

     This is just like making a regular message area, except�
you set one other thing. Make your area, say, MAIL. (The�
name is not important) Then, using the 1 command, designate�
it a mail area by changing the SYSTEMn.BBS for that area:

     1 1\A          Set attribute to 1
     1 S       Save that

     1 0\A sets a normal message only area (default) and 1�
1\A sets it as a Mail area. The only difference is in two�
commands.

     When the message areas are listed by the A command, the�
Mail area will be displayed with a *, and when in that area,�
the command prompt will say "FIDONET".

     The S (Statistics) command will list the available�
remote systems, in addition to the usual stuff.

     The E command (enter message) will prompt for the�
Destination System (node) before it asks for To:, Subject:,�
etc. However, this will not work until you make the�
nodelist, NODELIST.BBS, described later on. The actual�
operation of these is described in the BBS Manual Update.

     Note that the Mail area has it's own set of command�
privelege levels, (changeable via the 3 command) so that you�
can make E (enter message) SYSOP or EXTRA privelege level,�
to prevent unauthorized mail from being sent.
.pa
Making a Node List

     The node list is the list of remote systems, the phone�
numbers, etc. When you apply for a permanent node number,�
you will receive (in a message) the latest node list. Node�
lists will be broadcast to all FidoNodes as it is updated.

     NOTE: A slight oversight on my part: you must have your�
own node in the node list. Otherwise, you cannot leave a�
regular message in the mail section! Fidonet will not "call"�
your own system. Messages that are From: the node it was�
entered on do not get mailed.

     The node list, called NODELIST.BBS, describes each�
remote system, one per line. The node list is just an ASCII�
file, which can be created by PMATE, WordStar, etc. For�
example:

1  0  1200  Fido's_Board  1-(415)-864-1418  San_Francisco_CA

^  ^   ^    ^             ^                 ^
|  |   |    |             |                 |
|  |   |    |             |                 +--- City
|  |   |    |             +--------------------- Phone
|  |   |    +----------------------------------- Name
|  |   +---------------------------------------- Baud Rate
|  +-------------------------------------------- Cost
+----------------------------------------------- Node

     Each of these items are seperated by one or more spaces�
or tabs. Do NOT have spaces, commas or tabs in the middle of�
any of these.

Node

     This is that systems node number. This identifies the�
system mail is for (and from); it is buried in the mail�
packets, and if wrong, Fidonet will not accept that mail�
packet. It cannot be zero.

Cost

     This is the cost, in cents per minute, of the phone�
connection to this node. You can get this from your phone�
bill. Soon, I will start compiling these costs by getting�
information from the phone co. For now, estimate.

     Also, if 0, it is assumed to be a local call. If 0,�
then anyone may send messages to this node. Otherwise (if�
not zero) the user must have enough credit in their user�
record, or Fido will not allow them to enter mail. (Set by�
SYSOP.EXE; see SYSOP.DOC)

Baud Rate

     This is the speed to dial this system with when it is�
time to send them mail. It also is used in calculating the�
cost of a given message. It is any number that is a multiple�
of 300; i.e. 300, 600, 1200 ... 9600. For dialing purposes,�
1200 and up are dialed at 1200 baud, everything else is�
dialed at 300. Set 300 if your modem cannot handle 1200.

Name

     This is just the descriptive name (mnemonic) for this�
system. Luckily, most systems have some cutesy name, like�
Fido's Board, Demon, etc. It must be one word. (Use hyphens�
or underlines.) It must also be less than 14 characters long�
total.

Phone

     This is the phone number for the system. It is�
basically a standard D.C. Hayes SmartModem phone number,�
with one exception. If you use Sprint, etc, you must put it�
in each number. Do not leave spaces in the number. The legal�
characters in a phone number are:

     1,2,3,4,5,6,7,8,9,0 digits
     -              ignored
     ( )            ignored
     .              1 second delay

     Note that comma is not the delay character; it is used�
to seperate items in lists. A dot is translated to a comma�
when dialing. In addition:

     T              Touch Tone
     P              Pulse

     May be inserted at any point in the number as needed.�
Fidonet dials in Touch Tone by default, if not P is�
specified. The maximum length of the phone number is 39�
characters.
.pa
Modifying RUNBBS.BAT

     This is the final, and most important change of all.�
This defines when it is time to do Fidonet, and other�
things.

     An example of a good RUNBBS.BAT is:

     FIDO_IBM ..... 0400/Y 0030/W
     IF ERRORLEVEL 4 GOTO MAIL
     IF ERRORLEVEL 1 GOTO END
     RUNBBS
:MAIL
     NET_IBM ... 0400/Y 0030/W
     IF ERRORLEVEL 1 GOTO END
     RUNBBS
:END

     The first couple of lines should be familiar. Use�
whatever switches you have been using (time limits, /V,�
etc). You have to add two new ones:


     <time>/Y       FidoNet time
     <window>/W     Window width

     The time is the time of day that FidoNet traffic�
starts. This is currently fixed across the country due to�
the crude method of operation.

     The window is how long it does FidoNet traffic. This is�
currently one half hour.

     The times to use are:

 Pacific Time           Central Time Eastern Time
  0100/y                 0300/y       0400/y
  0030/w                 0030/w       0030/w

     NOTE: There is NO error checking on the times entered.�
It should be entered as 0100 for 1:00 AM. Also, it will NOT�
work if it crosses over midnight! 
.pa
Executing the FidoNet Program

     FidoNet is normally run from the RUNBBS.BAT batch file.�
It can also be run standalone. This chapter covers the�
command line switches to control Fidonet operation.

     Fidonet operates in a similar manner to Fido, in that�
all options are entered as command line arguments, the�
signon message, memory requirements, etc.

     Please see the chapter on FidoNet Operation for details�
on the use of FidoNet in a working syustem. This covers only�
the switches, and their effect on FidoNet.


Command Line Switches

<time>/Y Set Fidonet Mail Time

     This tells Fidonet (and Fido) when net time is. At this�
time, the net program si run, and processes mail. The times�
are currently fixed for each of the four time zones across�
the country. These times are:

Pacific             Central        Eastern
01:00 AM            03:00 AM       04:00 AM
30 minutes          30 minutes     30 minutes

     These times are entered as 100/Y, 300/Y, and 400/Y,�
respectively.


<number>/W    Set FidoNet Mail Window

     This controls how long it does mail. You must use 30/W.�
Between this and /Y, it says that mail is processed (as�
opposed to normal BBS operation) between 1:00 AM to 1:30 AM�
pacific time.


/X       No Outgoing Mail

     This can be used to stop all outgoing mail. If /X is�
present, no mail is sent (therefore no phone calls made)�
regardless of any messages waiting to be mailed.

     This can be used for non-standard modem that cant dial,�
Sysops who do not wish to allow outgoing mail for any�
reason. It is recomended that all Fidos run Fidonet, with�
this switch if necessary (called "ReadOnly") since bug�
notices, updates, etc will be broadcast over the net, which�
will probably be of interest to all Fido sysops.


<number>/V    Set Modem Carrier Detect Mask

     This has the same meaning as /V in the Fido command�
line, and must be set the same. See INSTALL.DOC for details.�
It controls which modem status bit Fidonet uses to detect�
incoming calls and loss of carrier.

/U       Suppress File Transfer Status

     If not present, FidoNet will display continuously the�
status of packet transfers, the same as Fido does up and�
downloads. Use /U unless you like looking at it.


/M       Resend (SENT) Messages

     This is ONLY for testing FidoNet, or could be used for�
to resend old mail. Normally, FidoNet will not send messages�
that have been sent before; this overrides that.


<number>/T    Set Connect Attempt Limit

     This controls how many times FidoNet will attempt to�
transfer a packet to a given machine. It is only applicable�
for attempts that actually get a "connect", i.e. calls that�
get through, not calls where the line is busy, no answer,�
etc. The intent of this is to prevent placing too many calls�
to a node that is not a FidoNet node, or hat is down, or is�
otherwise not able to handle FidoNet bu the modem answers.�
The default is six tries.

<number>/L    Change Redial Delay Modulo

     This controls the random time delay inbetween calling�
other nodes. The default is 2; if ther are no incoming�
calls, then Fidonet places calls (if needed) at a random�
interval of 1 or 2 minutes. This can be changed to between 1�
and any number of minutes. 

     Please do not change this, without a detailed analysis�
of the actual collisions detected, and without consulting me�
first. This number was chosen carefully, and results in�
optimal operation.

     This was included for test purposes, and for possible�
later field tuning of high traffic nodes.
.pa
Return to DOS: ERRORLEVEL Values

     When FidoNet time is over, FidoNet unpacks and packets�
received, and deletes its outgoing ones, if any, then�
returns to DOS, to allow RUNBBS.BAT to re-execute Fido.

     Fidonet returns result codes to DOS, to indicate what�
happened. These are:

ERRORLEVEL Values:

     0    Normal termination, run Fido
     1    Control-C typed, or Stack Overflow
     2    Fatal Disk error

     If ERRORLEVEL 0, then just run Fido the bulletin board.�
If any other value, than there was an error (or manual�
termination) and exit the batch file.